## Slide 1: Team 60: Solar Lighting Syste Bi-Weekly Update 3 Josh George, Jeb Malek, Lyric Haylow​ Sponsor: Dr. Wonhyeok Jang​ TA: Rhett Guthrie
Notes: Michelle

## Slide 2: Project Summary
A need for clean, renewable sources becomes more apparent than ever.
Our home indoor and outdoor lighting system is the first step towards this, using solar power.
Design an indoor/outdoor home lighting system that operates with a battery, power conversion, mobile application functionality, BT microcontroller for switch automation from motion sensors.
Notes: Kyle

## Slide 3: Project/Subsystem Overview
Notes: Eric

## Slide 4: Project Timeline
Subsystem Designs (completed 01/16) | Subsystems ordered and soldered (2/14) | Integration of Bluetooth and Arduino (to complete by 2/21) | Integration of Solar Charge Controller and MCU (3/9) | Final Integration (to complete by 3/15) | System Test (to complete by 3/21) | Validation (to complete by 3/25) | Demo and Report (to complete by 4/1)
Notes: Eric

## Slide 5: Solar Charge Controller
Accomplishments since last update 10 hrs of effort | Ongoing progress/problems and plans until the next presentation
PCB board soldered Gotten voltage output from one of the solar panels, confirmed working Preliminary datapoints for battery percentage attained. Likely wrong though. | Print 3D model for enclosure over Blitz Finish verifying necessary final values for Charge Controller Sun is temperamental and necessary for good testing.

## Slide 6
Time (AM) | Change in time (minutes) | Battery Voltage (Voltage
9:42 | 0 | 14.2
10:23 | 41 | 14
10:33 | 51 | 14.3
10:43 | 61 | 14.01
Solar Panel to battery testing using provided Charge Controller, introduces sun issues

## Slide 7: Inverter Subsystem Jeb Malek
Accomplishments since 403 25 hrs of effort | Ongoing progress/problems and plans until the next presentation
Power transformer voltage invalidated In-circuit serial programming issue | PCB Correction Ordering Corrected Version Assembly & Validation 12V – 5V Converter PCB Order
Evaluated Configuration Bits for Programming dsPIC
Speaking with sponsor about alternative changes to scope.

## Slide 8: Inverter Subsytem Jeb Malek
Verification DSPIC33FJ16504
Target Device ID Connection Issue
PCB Error Edit Ground Polygon Cutout / Via Solid Connections

## Slide 9: Inverter Subsytem Jeb Malek
Converter Schematic
Transformer Schematic

## Slide 10: Microcontroller Subsystem Jeb Malek & Josh George
Accomplishments since 403 20 hrs of effort | Ongoing progress/problems and plans until the next presentation
Passive Infared (PIR) Sensors Tested Coded microcontroller sensor relay information | Testing of Sensor proximity & distance Testing of Controlled Relay Communication with Arduino Testing of Relay with Light Load
Evaluated Sensor High & Low Communication Signal
Future Test Bluetooth App with relay control, receive of motion sense, sign of demonstration structuring

## Slide 11: Microcontroller Subsytem Jeb Malek & Josh George
PIR Motion Sensor Test

## Slide 12: Microcontroller Subsytem Jeb Malek & Josh George
Sensor 1 Reading Pin
Sensor 1 Lights

## Slide 13: Microcontroller Subsytem Jeb Malek & Josh George
Sensor 2 Reading Pin
Sensor 2 Lights

## Slide 14: Microcontroller Subsytem Jeb Malek & Josh George
Main error found during testing: Sensor 1 activates Sensor 2 lights too, and Sensor 2 activates sensor lights as well.

## Slide 15: Mobile Application Josh George
Accomplishments since last update 2 hrs of effort | Ongoing progress/problems and plans until the next presentation
-Added Bluetooth special characters functionality. | -Finish coding microcontroller sensor relay. -Add input pin option for solar charge controller.

## Slide 16: Mobile Application Josh George

## Slide 17: Execution Plan
Notes: Michelle

## Slide 18: Validation Plan